## Slide 1
The Robo-Medics
Joanna Dickinson, Lorena Ferreira, Erin Okuna,
Nick Sharp, Leanna Temple
1/29/19

## Slide 2
Objective:
To design a simple robot that will deliver prescribed pills to patient's rooms at specified times.
A 2002 study by the American Association of Medicine revealed 19% of doses are incorrectly delivered.
It is also common for patients to receive medication at the wrong times due to medical emergencies or insufficient staffing.
Possible customers include: hospitals, nursing homes, hospice care, etc.
Approach:
Navigate by placing RFID sensors in each room
UI for user-controlled schedule
Locked pill box requiring nurse code in order to access
Two independent motors control mobilization & turning
Sensors to detect obstacles
Budget and Schedule:
Budget:
Mechanical Components - $970
Electrical Components - $675
Estimated Total - $1,700 ($812 spent to date)
Total External Funding: $0
Schedule:
Initial Prototype Completed - March 10th
Final Prototype Completed - May 30th
Concept:
A robot that is placed within medical facilities and navigates to specific rooms at designated times to deliver medication to nurses/patients.
Pharmacist/nurse loads daily medications
into secured lockbox
Pill Bot autonomously delivers medications
to locations at specified times
Pictured Right: Concept robot
Pill Bot Robo-Medics: Joanna Dickinson (ME), Lorena Ferreira (ME), Erin Okuna (EE), Nick Sharp (CPE), Leanna Temple (ME)
Notes: Leanna

## Slide 3: Functional Specifications
Spec ID | Requirement | Threshold (Shall) | Objective (Should)
SS-01 | Lockbox Protection | Withstand at least 200 in-lb | Withstand at least 250 in-lb
SS-02 | Object Detection | 2.5ft | 4ft
SS-03 | Electrical Component Access | Will not be accessible during normal use | 
SS-04 | Nurse Verification | Unlock 75% of the time | Unlock 95% of the time
SS-05 | Cleanability | Will be sterilizable (will resist degradation by bleach and alcohol) | 
S-03 | Capacity | 12 Compartments | 24 Compartments
Safety and Security
Notes: Nick
Leanna

## Slide 4: Functional Specifications
Spec ID | Requirement | Threshold (Shall) | Objective (Should)
U-01 | Data Entry | Be equipped with a cable | Program wirelessly
U-02 | Medication Identification | Will have LED compartment indication | 
U-03 | Room Display | Screen will display correct room number | 
Ease of Use
Notes: Nick

## Slide 5: Functional Specifications
Spec ID | Requirement | Threshold (Shall) | Objective (Should)
E-01 | Speed | At least 1.5 ft/s | At least 2 ft/s
E-02 | Battery Usage | 4 hours w/o charge | 8 hours w/o charge
E-03 | Home Base | Within 3 ft of outlet | Within 1 ft of outlet
E-04 | Charging Time | Fully charge within 16 hrs | Fully charge within 8 hrs
Efficiency
Notes: Erin

## Slide 6: Functional Specifications
Spec ID | Requirement | Threshold (Shall) | Objective (Should)
M-01 | Stability | Support at least 45 lbs without tipping | Support at least 60 lbs without tipping
M-02 | Turning Radius | R < 2 ft | R = 0 ft
M-03 | Acceleration/Deceleration | At least 1 ft/s^2 | At least 1.5 ft/s^2
Maneuverability
Notes: Joanna

## Slide 7: Functional Specifications
Spec ID | Requirement | Threshold (Shall) | Objective (Should)
A-01 | Distance Calculation | 80% Accuracy | 95% Accuracy
A-02 | Navigation | Detect and process 80% of RFIDs scanned | Detect and process 95% of RFIDs scanned
A-03 | Room Verification | Correct room 90% of the time | Correct room 98% of the time
A-04 | Delivery Time | 3 min. Within scheduled delivery time | 1 min. Within scheduled delivery time
Accuracy
Notes: Nick

## Slide 8: Functional Specifications
Spec ID | Requirement | Threshold (Shall) | Objective (Should)
S-01 | Weight | < 60 lbs | < 45 lbs
S-02 | Dimensions | <24’’x 24’’x 40’’ (BxWxH) | <20’’x 20’’x 38’’ (BxWxH)
S-03 | Capacity | 12 compartments | 24 compartments
Size
Notes: Joanna

## Slide 9: Functional Specifications
Spec ID | Requirement | Threshold (Shall) | Objective (Should)
C-01 | Production Cost | < $1500 | < $1000
AP-01 | Visually Suitable | 60% | 85%
Cost and Appeal
Notes: Lorena

## Slide 10: Mechanical Drawings
Housing
Notes: Lorena

## Slide 11: Mechanical Drawings
Notes: Joanna

## Slide 12: Mechanical Drawings
Lockbox and Locking Mechanism
Notes: Leanna

## Slide 13: Mechanical Drawings
Notes: Leanna

## Slide 14: Mechanical Block Diagram
Notes: Leanna

## Slide 15: Electrical Block Diagram
Notes: Erin

## Slide 16: Software/Firmware Diagram
Notes: Nick

## Slide 17: PCB Design - Upper PCB
Notes: Erin

## Slide 18: PCB Design - Lower PCB
Notes: Erin

## Slide 19: PCB Receipt
*Combined PCB schematics and ordered with another group
Notes: Erin

## Slide 20: Engineering Analyses List
Mechanical Analyses
Torque
Motor Power
Heat Transfer
Stability
Center of Mass
Total Mass
Stress/Strain
Updated analyses in red, unchanged analyses in green
Electrical Analyses
Power Consumption
Power Capacity
Sensor Range
Notes: Lorena

## Slide 21: Total Mass Analysis
CAD model with appropriate assigned materials weighed: 40.40 lbs
Remaining materials estimations were made for:
    Pills: 0.5 lbs
    Individual bottles: 2.25 lbs
    Circuits and wiring: 5 lbs
Updated total is estimated to be 48.15 lbs
Notes: Joanna

## Slide 22: Center of Mass Analysis
Notes: Joanna

## Slide 23: Stress and Strain Analysis
Updated forces to analyze: 250 in*lbs using a small screwdriver, for 90th percentile male
RIT’S Edge Data
Notes: Leanna

## Slide 24: Power Capacity Analysis
Currents drawn during sleep mode and delivery mode were previously calculated under analyses for motor power and power capability.
When running the bot for an 8 hour shift, it is calculated that the battery will need a minimum capacity of 7.664 Ah.

## Slide 25: Project Demonstration Plan
At the end of winter quarter Robo-Medics will demonstrate an autonomous robot that:
Can hold its own weight plus the weight of medication.
Meets the above size and speed specifications.
Is able to navigate through a pre-programmed path/route.
Is able to detect objects in its environment and avoid collision.
Is equipped with a locking mechanism that opens the lockbox when an RFID card is scanned
The Robo-Medics are concerned about the lockbox protection, object detection, and appeal requirements. At the end of winter quarter the Robo-Medics will demonstrate that the medication delivery robot has the ability to detect objects, travel at specified velocities and move along a designated path. However, the navigation and object detection coding will be improved during spring quarter.
Notes: Nick

## Slide 26: Project Status
Next Components to Purchase:
Acrylic Plates
Acrylic Panels
Plastic welding adhesive
Waiting to obtain:
PSoC 6
PCB
According to schedule:
Current progress suggests that the objectives set forth this quarter are viable
Notes: Leanna

## Slide 27: Winter Schedule
*Completed tasks highlighted in green
Notes: Lorena

## Slide 28: Questions?